## Slide 1: Micro-ROS ROS-Industrial Spring Workshop May 7th 2018 Dr.-Ing. Ingo Lütkebohle, Bosch Corporate Research
Partially supported by EU grant 780785

## Slide 2: “In the future it should be possible to implement the ROS protocol directly on the devices embedded system” ROS2 Design Wiki “Stories”

## Slide 3: Robots are networks of devices
Micro-ROS
ROS
Micro-Processor
Linux
Firmware
Micro-Controller
Sensor/Actor
Serial/Bus
Image source: Erle Robotics, taken from OFERA proposal.
Motor Control MCU
Nav GPC
Safety MCU
Comm MCU
Wire Sensor
Wire Sensor
Image source: Bosch PowerTools GmbH, All rights reserved
Embedded
Focus Today

## Slide 4: Open Framework for Embedded Robot Applications (OFERA)
Micro-ROS
OFERA will extend ROS2 to allow its use in MCUs
https://ofera.eu/
The OFERA project is funded by the European Union‘s Horizon 2020 research and innovation programme under grant agreement No 780785
Microcontroller platform
RTOS
Additional device drivers
Scheduler extensions
RTOS abstractions
rmw_microxrcedss
rmw
ROS
Interop.
FIWARE
Interop.
Benchmarking
rcl
Predictable execution (scheduling)
Lifecycle and system modes
Embedded transform library
Application component
…
Application component

## Slide 5: Situation
Micro-ROS
ROS+Linux is a powerful combo
  Excellent libraries for perception, planning, networking, etc
  Unified developer eco-system: One kernel, most devices
  It’s what we all have on our desks
But…
  Issue 1: Hardware access
  Issue 2: Hard, low-latency RT
  Issue 3: Power saving
  Issue 4: Safety

## Slide 6: Real-Time Operating Systems (RTOSs)
Micro-ROS
RTOSs are optimized for real-time performance
In OFERA, we’re using NuttX as the default
  POSIX-style API makes porting easy
Other interesting choices include RIOT, FreeRTOS, Zephyr, etc
RTOS diversity is an issue
Hardware diversity is an even bigger issue
Something unifying would go a long way…

## Slide 7: New DDS-XRCE Standard
Micro-ROS
DDS-XRCE for eXtremely Resource Constrained Environments … brings DDS on MCUs
Client-server approach
  Power-saving
  Disconnected use
I’m assuming you heard a lot about it yesterday
Open-source at github.com/eProsima/Micro-XRCE-DDS

## Slide 8: Side-by-Side Comparison
Micro-ROS
 | ROS2 | Micro-ROS
Hardware | X86, ARM Cortex-A, … | ARM Cortex-M, ….
Resources | >512MB RAM, >8G Disk | ~100K RAM, ~1MB Flash
Communications | GBit/s, Ethernet, 802.11 WiFi | Serial, WPAN – 250k to 1MBit/s
Operating System | Linux, Windows, MacOS | RTOS (NuttX by default)
Middleware | DDS variant (by default) | XRCE-DDS (by default)
Middleware Abstraction | RMW | RMW
Client Support Library | RCL | RCL
Execution Layer | RCLCPP / RCLPY / … | RCL + RCLCPP
Executors | Generic | Custom

## Slide 9: Issue 1: Hardware access
Micro-ROS
Why not use Industrial PCs?
  You’re always talking to some piece of firmware over a comm link
  It usually doesn’t do exactly what you want
  There’s latency
Driver implementation…
  A multitude of serial protocols
  Almost as bad for field buses
  Often, important things (timing…) are not in the data-sheets
  State management for external devices is a mess
 We need to get into the firmware
ROS
Regular CPU
Linux
Firmware
Micro-Controller
Sensor/Actor
Serial/Bus

## Slide 10: Hacker-friendly single-board computers
Micro-ROS
Cortex-A class
  E.g., Raspberry Pi
  512MB RAM, SD card storage
  Reasonable set of I/O pins
  WIFI, BT, Ethernet, USB
  Linux capable
Arduino-class
  8/32 bit MCU
  4-16kB RAM
  Bare-metal
  Arduino I/Os
  Huge shield ecosystem
Cortex-M4 class
  E.g., STM32 IoT Discovery
  ~128kB RAM, 1MB flash
  Arduino-I/Os, PMOD
  Low-power networks
  Built-in sensors + I2C, SPI, etc

## Slide 11: Micro-Controllers: Hardware Access
Micro-ROS
Micro-Controller, n: Chip that contains a processor and peripherals
  analog/digital converters (ADC)
  Quadrature decoders (QED)
  PWM generators
  Digital IOs (GPIO)
  …
Buses with register support
  CAN, UART, SPI, I²C,…
  Register mapping for read/write
Much higher diversity and rate of evolution than general purpose CPUs
Image source: STMicro website, https://www.st.com/en/microcontrollers/stm32f479bi.html

## Slide 12: Issue 2: Status of RT on Linux
Micro-ROS
Linux scheduler has an RT class
  On a high-end PC, it gets you down to ~5μs task activation time
  But kernel processes can stall it
  Outliers up to tens of milliseconds
Linux PREEMPT-RT Patch solves this
  Can be difficult to integrate with other patches (e.g., BSP and proprietary drivers)
  This is after more than a decade of work
μs

## Slide 13: Example: Context Switch Time RTOS vs. Linux
Micro-ROS
Source: “PERFORMANCE ANALYSIS USING NXP’S I.MX RT1050 CROSSOVER PROCESSOR AND THE ZEPHYR™ OS”, MAUREEN HELM, LEOTESCU FLORIN, MARIUS CRISTIAN VLAD, NXP, 2018.
https://www.nxp.com/docs/en/training-reference-material/BENCHMARK-ZEPHYR-OS-PDF.pdf
cycles
cycles
Zephyr
Linux

## Slide 14: NuttX, the „Tiny Linux“
Micro-ROS
RTOS with POSIX API
  Released first in 2007 by Gregory Nutt
„Batteries included“
  Shell
  TCP/IP
    Incl. DHCP, NTP
  6LowPAN
  C++ standard libs: libcxx or uclibc++
  Many device drivers and BSPs
    Focused mainly on ARM, ARC, Atmel
  much more…
http://nuttx.org/
RTOS | POSIX? | libstdc++?
Zephyr | Threads, Time, IPC | No
ARM Mbed | No | No
FreeRTOS | Threads, Time | No
RIOT | Partial | ??

## Slide 15: NuttX Demo
Micro-ROS

## Slide 16: Issue 3: Power-saving
Micro-ROS
Power use is important in many embedded applications
  Battery-powered sensors
  Unmanned aerial vehicles
  Standby operation
Linux SBC use 1-2 orders of magnitude more power (Sources: http://www.pidramble.com/wiki/benchmarks/power-consumption, https://learn.adafruit.com/embedded-linux-board-comparison/power-usage, OFERA measurements)
Device | Idle | Operational
Rpi A | ~150mA | ~180mA
Rpi 3 | ~350mA | 500-800mA
STM32L1 | ~3mA | ~10mA
STM32F4 | ~10mA | ~100mA

## Slide 17: Issue 4: Safety
Micro-ROS
Being worked on since (at least) 2011
  SIL2Linux
  Project P
  …
SIL2Linux
  Target: Safety Integrity Level 2
    Strips much of Linux, most notably many drivers
    Going on for years, not clear what the outcome is
    But do watch https://elisa.tech/ !
  The highest SIL level is 4…
And then there’s the question of appropriate compute hardware
Image source: Carsten Emde, OSADL. Embedded World Presentation March 3rd 2011

## Slide 18: Open Source and Safety
Micro-ROS
Zephyr RTOS (a Linux Foundation project) attempts Safety Certification in 2019
Subset of whole OS
  Orange boxes: In scope for 2019
  Notably no drivers!
Based on existing work on security
Image source: https://events.linuxfoundation.org/wp-content/uploads/2018/07/OSLS-2019_-Zephyr-Project-.pdf

## Slide 19: CURRENT STATUS

## Slide 20: Target Devices
Micro-ROS
Device Classes
  Low-end: MCUs starting at 32kB RAM with low-power consumption
    E.g., STM32L1
  Typical: Cortex-M4 devices with ~100kB RAM
    E.g., STM32F4
Going below 32kB would likely require a different architectural approach and is not currently in scope
OFERA has two references boards with full OS support provided by partner Acutronic Link Robotics
  STM32L1-DISCOVERY
  OLIMEX STM32E407

## Slide 21: Turtlebot 2 Demo
Micro-ROS
micro-ROS running
- thin_kobuki_driver
- DDS-XRCE client at less than 100 KB RAM
DDS-XRCE over UDP
ROS 2 (Crystal) running
- Visualization
- Keyboard control - odometry to TF
- DDS <-> DDS-XRCE agent
Preliminary version at github.com/microROS/micro-ROS_kobuki_demo

## Slide 22: Turtlebot 2 Demo
Micro-ROS
Based on „thin kobuki“ driver
Converted to use rcl API
  rclcpp wasn‘t ready at the time
Porting issues?
  A few issues with C++ initialization

## Slide 23: Upcoming work

## Slide 24: Recap: Composable firmware
Micro-ROS
Nowadays, firmware provided by vendor
  Unforeseen features? Bad luck…
Vision: Add new features to existing firmware
  ROS2 way: Just add nodes
Challenge: Interference
  Need to make sure existing stuff still works!
Micro-ROS Approach:
  System Modes
  Domain-specific scheduling, towards providing guarantees

## Slide 25: Towards explicit architecture
Micro-ROS
CR/AEE1-Lange | 2019-03-29
© Robert Bosch GmbH 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
14
The OFERA project is funded by the European Union‘s Horizon 2020 research and innovation programme under grant agreement No 780785

## Slide 26: System Modes
Micro-ROS
CR/AEE1-Lange | 2019-03-29
© Robert Bosch GmbH 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
15
Introduces (sub-)systems hierarchy to ROS 2
Abstraction for hierarchical configuration, called system modes
Mode manager manages consistent, system-wide configuration
See microros.github.io/system_modes/
inference
observation
nodes
(sub-)systems
Mode Manager
model file
.yaml
subsystem 01
subsystem 02
system
lifecycle events
parameters events
mode change
request
The OFERA project is funded by the European Union‘s Horizon 2020 research and innovation programme under grant agreement No 780785

## Slide 27: Predictable Execution
Micro-ROS
CR/AEE1-Lange | 2019-03-29
© Robert Bosch GmbH 2016. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
16
First approach enables multiple executors per operating system process
Executors can be configured individually using standard scheduling mechanisms
Open-sourced prototype for ROS 2
See microros.github.io/real-time_executor/
Executor
Executor
Executor
OS Scheduler
Other node
…
…
Drive-Base node
onEmergencyStopMsg onCmdVel
publishWheelTicks reportDiagnosticsData
The OFERA project is funded by the European Union‘s Horizon 2020 research and innovation programme under grant agreement No 780785

## Slide 28: Domain-specific scheduling
Micro-ROS
Current real-time schedulers typically use priorities
  Not composable!
  Not domain-appropriate
Micro-ROS Approach: Domain-specific schedulers
  E.g., stage-based approach with „Sense-Plan-Act“
  Or more stages…
  Assign callbacks to stage using callback groups
  Derive within-group order from communication links
Provide „budgets“ by group
Sense
Laser
IMU
Plan
Obstacle Avoidance
Act
Velocity control
Report progress
Wheel Encoders
Model
Sensior Fusion
Mapping
Path Planning
Laser Driver
Read Scan
Diagnostics
Obstacle Avoidance
Update Map
Drive Base
Read Encoders
Speed Control
Scan Covariance
Compute Velocity

## Slide 29: Building micro-ROS…
Micro-ROS
Challenge: RTOS defines toolchain and system headers
  What‘s the build order?
Currently: ROS2 workspace built as part of NuttX build
  Pro: Handles toolchain (cross-compiling, etc.)
  Con: Time consuming
  Con: Workspace is not aware of being a micro-ROS target
Current work: Build everything using colcon
  NuttX vendor package to configure and build NuttX
  Colcon configuration to configure toolchain

## Slide 30: Building an ecosystem
Micro-ROS
Does this mean that every ROS developer can now start using MCUs?
Well…

## Slide 31: Further information
ROS 2 Embedded
microROS organization at GitHub
  https://micro-ros.github.io/
  https://github.com/micro-ROS/
OFERA website: https://ofera.eu/
ROS 2 Embedded Design Page
  Currently at https://github.com/ros2/design/pull/197
  After merge: http://design.ros2.org/articles/embedded.html

## Slide 32: Thank you